## Slide 1
FEEDBACK CONTROL OF A CHEMICAL REACTOR USING PID CONTROLLER
PAGE 01
PROCESS CONTROL AND AI APPLICATIONS : CHL4020
By Group -02
Devang Dobliyal (B21CH007)
Harsh Raj (B21CH008)
Jahnavi Pandey (B21CH010)
Kachhawa Goutham (B21CH011)

## Slide 2
REACTOR:
#AD6237
PAGE 02
CSTR (Continuous Stirred Tank Reactor)
CONTROL VARIABLE:
Temperature
CONTROLLERS USED:
PID Controller
Fuzzy Controller

## Slide 3
PAGE 03
Motivation
  The Continuous Stirred Tank Reactor (CSTR) control problem is particularly controversial due to its non-linear dynamics.
  Increasing energy costs are driving the need for thermally integrated processes.
  safety measures to prevent the issues in the chemical plants are important in ensuring the plant’s normal operation.
  There is a critical need for advanced control systems in industrial processes.
  Fuzzy logic offers low computational cost and flexibility in handling complex non-linear issues, providing approximate reasoning over traditional crisp assumption models in real-world applications.

## Slide 4
#AD6237
PAGE 04
  Initial efforts in developing mathematical models for process control, focusing on mass and energy balance.
1950
1960
1970
1990
2010
  Introduction of control strategies based on non-linear models.
  Implementation of PID control systems and the advent of adaptive control techniques.
  Emergence of advanced control methodologies including neural networks, fuzzy logic, and model predictive control (MPC).
  Application of artificial neural networks (ANN) and genetic algorithms for process control optimization.
Previous Attempts

## Slide 5
PAGE 05
Industrial Application
  Oil and Gas: They manage flow rates, pressure, and temperatures in pipelines, refineries, and processing plants.
  Food and Beverage: Temperature control in pasteurization processes and environmental conditions in fermentation processes are managed by PID controllers.
  Pharmaceuticals: PID and fuzzy controllers regulate critical variables such as temperature, pressure.
  Petrochemicals: PID controllers are widely used in the petrochemical industry for process control, while fuzzy controllers handle more complex and adaptive scenarios.
  Plastics Manufacturing: In plastics manufacturing, PID controllers manage simple tasks, while fuzzy controllers handle complex, multivariable processes like polymerization.

## Slide 6
PAGE 06
CSTR Modeling and Transfer Function
Assumptions:
  It is perfectly agitated.
  The mass densities of the input component and that produced are equal and identical.
  The volume of liquid ܸin the reactor is kept constant.
  Rate of Reaction : r = k*Ca
  where k is given by equation:
K=Ko*exp(Ea/R*Tr)
.

## Slide 7
PAGE 07
Open Loop System
Block diagram for open loop system
Results:

## Slide 8
Block diagram for PID Controller
PAGE 08
Closed loop without tuning
Results:
Parameters:
P = 1
I = 1
D = 0

## Slide 9
PAGE 09
PID Controller : Auto Tuning
Tuned Parameters:
P = 4.17169602708866
I = 50.9712560094397
D = -0.00301394977236811
Results:

## Slide 10
PAGE 10
PID Controller : Re-Tuning
Results:

## Slide 11
PAGE 11
PID Controller : Comparison
Combined Block diagram
Combined Results

## Slide 12
PAGE 12
Fuzzy Controller
Block diagram for Fuzzy Controller

## Slide 13
PAGE 13
NEED
FOR
DERIVATIVE
NEED
FOR
INTEGRATOR
  Reduces overshoot and improves stability.
  Quickens the system's reaction to sudden changes.
  Predicts and responds to rate of change in errors, helping to prevent future ones.
  Integrates the error over time, addressing any continuous offset that remains after the initial control actions.
  Corrects steady state errors.
  To improve system's accuracy
  To eliminate any long-term bias in the control signal .
Fuzzy Controller

## Slide 14
PAGE 15
Fuzzy Controller : Member Functions
What is Member Function?
  A membership function in fuzzy logic quantifies the degree of membership of an input value to a specific fuzzy set.
  Membership degree ranges from 0 to 1, with 0 indicating no membership and 1 indicating full membership.
  Values between 0 and 1 represent partial membership, reflecting partial alignment with the set's characteristics.
  Triangular membership functions are commonly used due to their simplicity and ease of interpretation.
  The triangular membership function is represented by a triangular shape.
  It is defined by three parameters: 'a', 'b', and 'c', representing the minimum, peak, and maximum values of the fuzzy set, respectively.
  The 'b' parameter indicates the center point or peak of the fuzzy set.

## Slide 15
PAGE 16
Fuzzy Controller : Member Functions
Input : E , dE

## Slide 16
PAGE 17
Fuzzy Controller : Member Functions
Output : S

## Slide 17
PAGE 14
Fuzzy Controller : Rules
  Define input and output variables and their linguistic terms.
  Create IF-THEN rules based on expert knowledge or data analysis.
  Convert crisp inputs to fuzzy sets using assigned membership functions (fuzzification).
  Evaluate rules based on current fuzzy input values (fuzzy inference).
  Convert fuzzy output back to crisp values for practical application (defuzzification).

## Slide 18
PAGE 18
Fuzzy Controller : Control Surface
Fuzzy Control Surface

## Slide 19
PAGE 19
  The closed loop fuzzy control provides the most accurate control with no overshoot and fast settling time.
  The closed loop PID control is faster than open loop but has a slight overshoot before settling at the reference temperature.
  The open loop control system is the slowest and does not reach the reference temperature.
Comparison: PID vs Fuzzy

## Slide 20
PAGE 20
Comparison: PID vs Fuzzy
Control Logic
Criteria
PID Controller
Fuzzy Controller
Linear, model based requires a mathematical model
Model-free, based on rule sets and human reasoning
Tuning
Parameters (P, I, D) need manual tuning
Parameters self update depending on the rules given
Overshoot
Exhibits greater overshoot in comparison
Minimal to no overshoot produced
Robustness
Robust to certain types of disturbances and uncertainties
Extremely robust, especially with high levels of uncertainty
Implementation
Relatively easy to implement in hardware and software
Can be more challenging to implement effectively

## Slide 21
Adaptive Control Strategies Comparison
Strategies implemented :
RLS(Relative Least Square)
ABC (Artificial Bee Colony)

## Slide 22
PAGE 24
Conclusion
  In comparing the performance for various adaptive strategies we can observe that the performance of RLS is best followed by ABC. Both adaptive methods outperform the traditional PID tuning method.
  The developed approach has broad applicability across industries such as chemical, pharmaceutical, and biotechnology for managing the CSTR system and improving process efficiency and quality.

## Slide 23
PAGE 25
Thank You